## Slide 1: nRF51822 Features
32-bit ARM Cortex M0 processor
256kB flash/ 16 kB RAM
31 GPIO pins
2 SPI channels
2.4 GHz radio
  Programmable output power +4dBm to -20dBm
  Tx and Rx radio can be enable separatly
16 MHz oscillator
GFSK Modulation
2 Mbps maximum On-air data rate
-85dBm at 2 Mbps sensitivity
Selectable peripheral module On/OFF
  2 uA when all peripherals in IDLE and CPU OFF

## Slide 2
Electrical Characteristic (Processor)
  VDD = 3.0v
  I @ 16MHZ running off flash memory = 4.4 mA
Electrical Characteristic (Radio 2.4 ghz)
  VDD = 3.0v
  Tx Current @ +4dbm = 16 mA
  Tx Current @ -16dbm = 6 mA
  Rx Current @ 1 mbps = 13 mA
Electrical Characteristic (SPI)
  VDD = 3.0v
  Current @ 125kbps = 180 uA
  Current @ 8 Mbps = 200 uA
Mechanical Characteristic
  L x W x H = 6 x 6 x .85 (mm)
nRF51822 Characteristic

## Slide 3: nRF51822 Block Digram