## Slide 1
RHD2000 Features
Fully Integrated Electrophysiology front end chip
16-bit ADC
  30 kSamples/s/channel
32 or 16 channel input
  16 channel differential input
SPI interface with microcontroller
Low input-referred noise: 2.4 uV
DSP to filter out DC noise
Adjustable lower and upper cutoff frequency
Each amplifier on/off controable
  Each amplifier consumes: 7.6uA/kHz
    Based on upper cutoff frequency

## Slide 2: RHD2000 Characteristic
Electrical Characteristic
  VDD = 3.3v
  Baseline Amplifer current = 200 uA
  Amplifier current = 7.6uA/kHz
  Baseline ADC current = 510uA
  ADC current = 2.14uA/(kS/s)
  SPI current = 40 uA
Mechanical Characteristic
  L x W x H = 8 x 8 x 0.85 (mm)

## Slide 3: RHD2216 Block Diagram

## Slide 4: RHD2000 Timing Diagram

## Slide 5: RHD2000 Interface with nRF51822