## Slide 1: Testbed #3
3) Closed-loop Brain-controlled Interfaces: The center is focused on developing brain-controlled interfaces that assist individuals with movement impairments. Examples include remote assistive devices controlled by brain signals, and closed-loop systems were sensory information or motor intent is routed back into the nervous system via stimulation. Proposals that advance our ability to reliably record signals originating from the brain, extract useful control commands in real-time, and actuate an external device or deliver functional stimulation to the sensorimotor system are encouraged.

## Slide 2: Closed-loop Brain-controlled Interfaces Block Diagram (overall)
A: Central Neural Interface - Record (wirelessly) signals originating from the brain
B: Brain Neural Signal Translation - Extract useful control commands in real-time
C: Robust Control of Remote System - Actuate remote assistive devices
D: Functional Electrical Stimulator - Deliver functional stimulation
E: Sensory Feedback - Motor intent is routed back into the nervous system via stimulation

## Slide 3
System Specs for BCI Test-Bed
Phase | System Specs |  |  |  |  |  |  |  | Outcomes Goals
 | Power | Surface Area | Weight | CMOS Technology | Wireless Technology | Electrodes | Data Transmission Tech. | Distance | 
Phase 1 | 0.5 mW – 1mW (5V, mA) |  |  | MOSIS IBM – 45 nm to 0.25 µm TSMC - 40 nm to 0.35 µm |  | Thin-film (ECoG) 5x5 array | IR, Optical | 5m – 10m | 
Phase 2 | 100 uW 1V, mA |  |  | 22 nm |  | Thin-film (ECoG) 10x10 array | Optical | 30m – 50m | 
 | Energy Harvesting |  |  |  |  |  |  |  | 
Phase 3 | <100 uW (ultra low-power) Energy Harvesting |  |  | 22 nm or less | WBN | Deep electrodes (3D) with multi-sites (10x10 array) |  | > 50m | 

## Slide 4
Push |  | Test Bed | Pull | 
Basic Science | Details |  | Technology Need | Details
Electrodes & Other Neural Interfaces |  | BCI Test Bed (2) | Implantable ECoG | 
Communications & Interfaces | Signal Processing |  | Implantable FES | 
 | Pre-Processing (Pre-amp, filters, etc) |  |  | 
 | Compression/Multiplexing |  | Wearable EEG | 
 | Power |  |  | 
 | Neural Signal Translation |  | Flexible Electronics | 
 | High-Level Intent Extraction |  |  | 
Movement Control Theory | Algorithms |  |  | 
 | BioMechanical Control |  |  | 
Movement Stimulation |  |  |  | 
Sensory Feedback | Visual Feedback |  |  | 
 | Tactile Feedback |  |  | 
 | Other Feedback mechanism(s) |  |  | 
Brain Adaptation | Neural Feedback Adaptation Strategy |  |  | 
System Definitions for BCI Test-Bed

## Slide 5
Center for Sensorimotor Neural Engineering
BCI- SDSU
SDSU Mobile EEG
High-aspect ratio E-COG electrode
Artifact removal algorithm
3D gel-impregnated EEG electrode